## Slide 1
ranbsingh
Laboratory Information Management

## Slide 2
Laboratory Information
the sole product of any laboratory
Laboratory Informatics
the specialized application of information technology to optimize and extend laboratory operations
ranbsingh

## Slide 3
Traditional Functions of
Laboratory Notebooks
Record experimental conditions
Store primary laboratory data
Note experimental observations
Give reference to external data
Make interpretations
Draw conclusions
Provide legal record (for intellectual property)
ranbsingh

## Slide 4
Concepts of
Laboratory information management system
LIMS are a set of computer based methods used by a laboratory to manage its data and disperse the results to designated areas
-software and hardware solutions
There is no standard LIMS
-in house customized LIMS
-tailored to the protocols and processes
ranbsingh

## Slide 5
Those who benefit from LIMS
Scientists
Data analysis and data management
Lab managers
Data management not notebook management
Compliance and regulatory auditors
Complete audit trail with no paper chase
QA/QC
Concurrent accessibility of all data
IP Hawks
Complete legal records for litigation support
ranbsingh

## Slide 6
LIMS requirements for Analytical Laboratories
Tracking
-Samples, reports etc
Scheduling
-Tests, equipment maintenance
Quality Assurance
-Validation in QA/QC
Data access and sharing
-instrument interfacing
-Customer centered reporting
ranbsingh

## Slide 7
role of forensic science laboratory
to provide information for
investigative
judicial
decision
making
and
quick
reliable
information
decision
efficient
effective
ranbsingh

## Slide 8
★ automation of information
production and distribution
for effective and efficient delivery of justice,
- the data and information should be shared between partners of the Criminal Justice System
- by integrating their Computer Applications
Laboratory Information Management
ranbsingh

## Slide 9
Objective of
Information Management Program in Forensic Science
to enhance the ability to
prevent and solve crimes
ranbsingh

## Slide 10
Do you have to repeatedly and manually write
the case information to the top of every page?
Do you know…
Where are the specimens?
What is the testing status?
Who worked on the case? When?
How can you guarantee the lab processes
follow the protocols?
How do you track a bad reagent lot?
What is the performance quality of the
lab processes?
How can you track and monitor lab
performance in real time?
Does your analyst have all the information readily
available and organized for courtroom testimony?
ranbsingh

## Slide 11
Improve
Your Laboratory Performance with
Laboratory Information Management
Enforce Standard Operating Procedures
Conform to General Laboratory Practice
Minimize Paper-Based Operations
Efficient System Response
Direct Access to Critical Information
Retain Data Storage Integrity
Increase Laboratory Throughput
ranbsingh

## Slide 12
Operational Methods of
Computerized Instruments
computers are used in conjunction with
analytical measurements in three ways
Off-line
On-line
In-line
ranbsingh

## Slide 13
Off - line
human
operator
analytical
instrument
computer
and
mass storage
Data is collected by human operator
and
transferred to computer for processing
ranbsingh

## Slide 14
On - line
analytical
instrument
human
operator
computer
and
mass storage
Direct communication between the instrument and the computer
(by means of electronic interface, signal digitization, and storage)
Computer remains a distinct entity with provision for
mass storage of data and instruction for processing the data
Off-line operation is also possible with this arrangement
ranbsingh

## Slide 15
In - line
analytical
instrument
human
operator
computer
and
mass storage
A microcomputer or a microprocessor is imbedded in the instrument
The operator communicates with and directs the instrument operation
via computer
The operator does not, however, necessarily program the computer
In in-line and on-line operations, the data are often transferred to
the computer in real-time. Real time processing involves data
treatment performed simultaneously with data acquisition
ranbsingh

## Slide 16
Laboratory Information Management System
Classification of LIMS function
The system related category
• Data repository - database management system (DBMS)
The user related functional categories
• Data capture - the gathering of data
• Analysis of data - reduction & manipulation of data
• Reporting - presentation of data
• Management - management of data and the laboratory
ranbsingh
An integrated computer based system combining
data capture, data analysis, reporting and management
functions that is linked by a common data repository,
to meet the needs of a laboratory environment

## Slide 17
laboratory
information
System
(DBMS)
data
capture
analysis of data
reporting
management
ranbsingh
Purpose
• to collate sample information with
associated analytical information
• to reduce the administration
associated with reporting results
these are merged via a database

## Slide 18
Levels of complexity in functional areas
Level I Minimum functions
(usually manual, minimal help of technology)
Level II Intermediate functions
(known applications, generally automated
functions)
Level III Advanced functions
(cutting edge technology, high risk and cost)
ranbsingh

## Slide 19
Data Capture
Level I
Manual entry of sample information
Manual result entry with verification
Level II
Online data capture from instrument
Use of bar code readers
Level III
Bidirectional Communication
– files (method parameters, run lists etc)
downloaded from LIMS and result files uploaded
electronic transfer of files containing
data reports from instruments to the LIMS
ranbsingh

## Slide 20
Data Analysis
Level I
Verification of data format entered into LIMS
Calculation of results –Automatic calculations
on data entered manually or online
Level II
Transfer of result files to statistical & interpretive packages
Data reduction program – calibration curves, concentration etc
Interpretation of results – graphics etc to visualize data & results
Data conversion from instruments to database management system
Level III
Substructure searches
Conversion of data to information – artificial intelligence
3 - dimensional graphics
ranbsingh

## Slide 21
Reporting
Level I
Hard coded reports –reports are defined and coded, only values are entered
Data base searching via forms
Comparison of results with predefined specifications
Level II
User configured reports
Graphical representation of results
Ad hoc searching and reporting
Internal electronic distribution of reports
Interfacing with desktop publishing packages
Chemical structure drawing
Level III
Natural language reporting methods
Expert assistance for ad hoc reports
ranbsingh

## Slide 22
Management
Level I
Sample log-in, and acknowledgement of sample receipt
Sample and status tracking – backlog reports
Worksheet production
Archiving retrieval of data via magnetic media
Approval and validation schemes for results
Stand alone error reporting, and Hierarchical security
Level II
Location of samples
Estimation and scheduling of work
Audit trail of data base
Transaction logging, and Class security
Level III
Resource management
Online scheduling of work from other systems
Electronic laboratory notebooks
Error correction by use of expert systems
Dynamic balancing of laboratory resources
ranbsingh

## Slide 23
Review of the laboratory
• Laboratory interaction
• Workloads
• Staff productivity
• Sample receipt
• Work scheduling
• Sample preparation
• Analytical methods
• Calculation of results
• Internal references
• Collation of information
• Interpretation (opinion)
• Reporting
ranbsingh

## Slide 24
Source of LIMS
three main approaches
Purchase a system from a
commercial vendor
laboratory may have to undergo significant changes in order to
conform to the product purchased
Use a software house (company)
to write the system
average software professional does not usually have the background to effectively interpret laboratory’s requirement
ranbsingh
LIMS are a set of computer-based methods used by
a laboratory to manage its data and report the results

## Slide 25
Source of LIMS
In-house development of the system
flexibility, adaptability, ease of evolution,
and support
ranbsingh
LIMS are a set of computer-based methods used by
a laboratory to manage its data and report the results
There is no “Standard” LIMS
In-house customized, configured LIMS
tailored to lab protocols and processes
Bench personnel must be taught to use LIMS
Consistency of approach builds team work
All scientists/officials must have their
own access point

## Slide 26
Common issues for LIMS implementation
Most LIMS products allow the laboratory to;
register work requests;
print analytical worksheets;
monitor and communicate sample/
technique backlogs;
schedule work;
acquire and store analytical data;
monitor the quality of all analytical work;
ranbsingh

## Slide 27
Common issues for LIMS implementation
approve analytical data for client release;
print and store analytical reports and invoices;
protect the security of all data;
track and locate samples in storage;
track and communicate all quality
control in the laboratory;
provide laboratory management
-with production and financial statistics and
-with client information, e.g., names,
addresses, sales figures, etc.
ranbsingh

## Slide 28
An appropriately designed and installed LIMS can quickly bring accuracy and accessibility to the flow of samples and data in any laboratory.
The real value of a LIMS is the ability to maximize sample throughput and minimize labor costs.
ranbsingh

## Slide 29
Facilitation of
Laboratory Operations
Receipt of cases
Allotment of cases
Job assignments
Progress tracking
Results entry
Results verification
Reporting
ranbsingh

## Slide 30
Audit Trail
a chronological record of
when users log-in,
how long they are engaged,
what they were doing,
whether any actual or attempted
security violation occurred
that may enable the reconstruction and
examination of a sequence of events
ranbsingh